## Slide 1: Reliable connectivity for a dime
Vamsi Talla, Mehrdad Hessar, Bryce Kellogg, Ali Najafi,
Joshua R. Smith and Shyamnath Gollakota

## Slide 2: Ubiquitous Connectivity

## Slide 3
What do we need to enable ubiquitous connectivity?
Cost
Power consumption
Size and form factor
Coverage and operating distances

## Slide 4
Hypothesis: No technology exists today which satisfy these requirements
Active Radios
RFID
$2-$4 price point
Consumes 10-1000 mW
Incompatible with printed batteries & require external components
Wide area coverage including through wall propagation
Costs <10 cents
uW power budget
Small flexible sticker form factor & low peak currents
Short range and does not work through walls and obstacles
Can we get the best of both worlds?

## Slide 5
Achieve data rate from 50 bps to 32.5 kbps
Whole home sensing, precision agriculture and implanted flexible medical devices applications
First wireless system that operates at km distances while consuming less than 10 µW

## Slide 6
Backscatter Communication

## Slide 7
d1
d2
Backscatter Device
RF Source
Receiver
Challenge: Signal Propagation in Backscatter Systems
RF carrier
9

## Slide 8
d1
d2
Backscatter Device
RF Source
Receiver
Challenge: Signal Propagation in Backscatter Systems
d
Extremely low signal strength data packet and a strong blocker at the receiver

## Slide 9
Our Solution: Clean slate design of backscatter system
Use coding to achieve optimal tradeoff between sensitivity and data rate
Modulation scheme resilient to single tone interference
Chirp Spread Spectrum Modulation
Decode signals down to -148 dBm
50 bps to 32.5 kbps data rates
Blocking immunity of 90 dB

## Slide 10
Chirp spread spectrum modulation
Linearly vary the frequency of the carrier with time
Bit ‘0’
Bit ‘1’
Data is encoded in cyclic shifts of frequency

## Slide 11
Synthesize CSS using backscatter
Linearly vary the frequency of the square wave at the backscatter switch

## Slide 12
d1
Synthesize CSS using backscatter
9
CSS Modulated Data packet
Backscatter Device
RF Source
Receiver
Extremely small, low power and cheap long range connectivity solution which can be embedded in every object

## Slide 13: Implementation
COTS Prototype:
MicroSemi Igloo Nano FPGA
Custom RF backscatter switch
IC Implementation:
TSMC 65nm LP Process
Verilog baseband, RF switch & PLL
Consumes 9.5 µW during transmission

## Slide 14
Evaluation
Tested our system in various wide area deployments including open roads/fields and Lake Washington.
When the RF source and receiver are separated by 475 m, the backscatter device can be placed anywhere between the two.
Backscatter device and RF source are co-located, the receiver can be as far as 2.8 km.

## Slide 15
Live Demo

## Slide 16: Applications
Wide area deployments:
Home & Office sensing
Precision Agriculture
Implanted & Medical devices:
Contact Lens
Epidermal Patch Sensors

## Slide 17
Reliable Connectivity across
  3 floor ~5000 ft2 home
  13,000 ft2 office spread across 41 rooms
Home and Office Sensing

## Slide 18
Precision Agriculture
Reliable communication across a 1 acre farm

## Slide 19
Implants & Flexible Medical Devices
Flexible Epidermal Patch
Smart Contact Lens
Biological tissue attenuates RF and significantly detunes the antenna

## Slide 20
Smart Contact Lens & Flexible Epidermal Patch
Connectivity across the entire 3,328 ft2 atrium
Tx
Rx
104 ft.
32 ft.

## Slide 21
Conclusion
Inexpensive flexible form factor connectivity solutions which can be integrated into everyday objects.
Demonstrate whole home coverage, agriculture and long range implanted medical applications.
First wireless system that operates at km distances while consuming less than 10 µW.

## Slide 22
jeevawireless.com
longrange.cs.washington.edu
Contact us at
info@jeevawireless.com

## Slide 23
The case for backscatter communication
  Power consumption
    1000x – 10,000x lower than radios
  Cost & Size
    Small size with minimal analog front end
    No external crystals or other components required
  Battery technology
    Low peak current: compatible with flexible printed battery technology
Extremely small, low power and cheap connectivity solution which can be embedded in every object